## Slide 1: Shift Registers Arduino & 7 Segment LED Displays
Presented by: Chris Chaney
christopher_chaney@homedepot.com

## Slide 2: Who is this guy?
Chris Chaney
  Software Engineer for 20 years
  Lead Developer @ HomeDepot.com
  Tinkerer with all things electronic and mechanical
  Spends spare time with…
    My aging motorcycle
    My box of Arduinos and electric goodies
    Any computer I can get my hands on

## Slide 3: Who are you?
What experience do we have in the room?
  Arduino?
  Basic electric components? (LEDs, Resistors, capacitors)
  C, C++, or Java?

## Slide 4: What is a Shift Register?
In digital circuits, a shift register is a cascade of flip flops, sharing the same clock, in which the output of each flip-flop is connected to the "data" input of the next flip-flop in the chain, resulting in a circuit that shifts by one position the "bit array" stored in it, shifting in the data present at its input ...

## Slide 6: TL;DR
Shift registers are a set of storage compartments with the exit of compartment connected to the entrance of another. This set of connected compartments creates an array of data that can only be fed from one direction.
0
1
1
0
1
1
0
1
1
0
Step 1
Step 2
0
1
0
1
0
Step 3
1
0

## Slide 7: 74HC595 : Much more than a pretty face

## Slide 8: The 74HC595 “Schwifty” has…
  An 8 bit shift register with a single overflow bit
  An 8 bit storage register that can be activated in parallel
  Cool functions like..
    Master register clear
    Output disable

## Slide 9: Let’s get Schwifty!
The Players….
  SER– Serial Input
  OE – Output Enable
  RCLK – Register Clock
  SRCLK – Serial Clock
  SRCLR – Serial Clear (or MR / Master Reset)

## Slide 10: The Rules of “Schwifty”

## Slide 11: The Arduino
An open source microcontroller with amazing capabilities.
What we need to know for this talk….
  Arduino runs code sent to it our computers via USB cables
  We will use the official Arduino IDE to write our code
  Arduino outputs 5 volts enough to power small projects

## Slide 12: 7 Segment displays
  Made of LEDs (Light Emitting Diode)
  ALWAYS use resistors (220ohm-330ohm)
  Careful bringing them into Irving, TX
  Notice the clockwise pattern of the segments (ignore the dot for now)

## Slide 13: 7 Segment display common anode wiring
+
+
a
b
o
c
+
d
e
f
g

## Slide 14
+
+
a
b
o
c
+
d
e
f
g

## Slide 15: What we’re building!
Arduino driving a shift register to run a 7 segment LED display.
Why use the shift register? We could just connect the display to 7 Arduino leads.
Yes, but then you could only drive one display. This setup, and the use of the overflow register can drive 4 displays safely.

## Slide 16: Get the tools and code
Fritzing (optional, but HIGHLY recommended)
  http://fritzing.org/download/0.9.2b/
Arduino IDE
  https://www.arduino.cc/en/Main/Software
The code and Fritznig file for the session
  https://github.com/cechaney/Maker-Visit-Code.git

## Slide 17: Fritzing follow-along for wiring

## Slide 18: Arduino IDE follow along

## Slide 19: Debugging and play